## Slide 1: SRI TA1 NuSymCORE
Principal Investigator: Susmit Jha
Team: Adam Cobb, Daniel Elenius, Anirban Roy, Kaushik Koneripalli, Chris McComb
Neurosymbolic Computing and Intelligence (NuSCI))
Computer Science Laboratory, SRI
Prepared for: Dr. Matthew Wilding, DARPA I20
Date: December 12, 2022
DARPA Symbiotic Design for Cyber Physical Systems
This research was developed with funding from the Defense Advanced Research Projects Agency (DARPA). The views, opinions and/or findings expressed are those of the author and should not be interpreted as representing the official views or policies of the Department of Defense or the U.S. Government. This research was supported by Contract No. FA8750-20-C-002.

## Slide 2: Talk Outline
Key Challenges in CPS Design and Desiderata of an AI Co-Designer
Overview of Trinity AI Co-Designer
  Invertible Neural Networks
  Hamiltonian MCMC over Uncertainty-quantified Generative VAE Model
  Neuro-symbolic Generator Using Language Models for Symbiosis
Results on Program (TA3) Corpus and Hackathons: Athens and Nautilus
  Top-down Design for Athens
  Bottom-up Design for Nautilus
Conclusion
  Program Metrics
  TA2 Interaction
  Publications
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 3: Key Challenges in CPS Design and Desiderata of an AI Co-Designer
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 4: Design is a Sequential and Iterative Decision-Making Process
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 5: Design is a Sequential and Iterative Decision-Making Process
Design process is a sequential and iterative decision-making process.
Incomplete specification that is refined during the design process. Need to avoid over-concretization.
  In place of single optimum design, discover a diverse set of designs.
Compositional representation and exploration of design
  Hierarchy of parts and subsystems. E.g., faring and pressure-vessel design in UUV design
  Composition of aspects / domains / physics. E.g., design of propulsion subsystem, pitch/roll subsystem
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 6
Hierarchical Multi-fidelity Surrogate Models
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 7: AI-driven Design needs Hierarchical Multi-fidelity Surrogate Models
AI codesigner can query models (physics or ML-based) or humans as oracles to guide their decision steps.
Physics-based scientific models (e.g., computational fluid dynamics models) are slow to evaluate.
Need to accelerate these models with learned hierarchical surrogates.
    The accuracy/fidelity/cost of learned surrogates are different at different stages of the design.
    Some design-decisions need component/subsystem-specific surrogate model.
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 8
Learn
Sample
Filter
Reuse Knowledge and Learn from Small Data
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 9: AI-codesigner needs to reuse knowledge and learn from small data
AI codesigner needs to reuse existing domain knowledge : basic physics, domain-specific design rules, human intuition such as seed designs.
Evaluation of design is costly, and the number of design epochs are few. Hence, AI co-designer needs to learn from small data.
  Need methods to filter and lift failures to rules.
  Need for smarter and adaptive data-generation
The AI designer needs to not just optimize for a single design problem against a fixed specification but instead be an adaptive agent learning across design iterations and problems.
Learn
Sample
Filter
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 10: Overview of Trinity AI Co-Designer
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 11
Invertible Deep Surrogates
Physics-guided Invertible Neural Network
Encoder: learned
or fixed
Decoder
Invertible Neural Networks
Design
Design
Design Objectives
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 12: Design as an Inverse Problem
Inverse problem: Generate design corresponding to a given design objective
In many applications, the forward scientific model can be slow/expensive and can only be sparsely sampled, thus an inverse model can help generate novel designs with desired specifications
While the forward model is well-defined and can be approximated in a supervised learning setup, the inverse problem is ill-defined due to the ‘many-to-one’ mapping from inputs to outputs.
X
Design
(latent space / parameters)
y
Output
(design objectives / measurements)
Forward prediction
Backward inversion
Scientific Models
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 13: Invertible Neural Networks
As there is an information loss during the forward process f(x ->y), latent variable (z) is introduced to capture the information about X that is not present in y
This allows to learn the inverse process as:
where f() and g() are modeled by invertible neural networks
Useful for motor-propeller-battery choice (propulsion subsystem for UAV) + Fairing Design for UUV
Invertible neural network framework with inputs (X), outputs (y) and latent variable (z)
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 14: Example Application: Fairing design
The goal of fairing design is to generate shapes that
  experience less drag forces,
  pack the required components, and
  efficiently navigate (good controllability) through the mission path
We consider a parametric representation of fairing shapes
  Parameters control various aspects of the fairing such as nose shape and length, tail shape and length, size and length of the body, curvatures of the body etc.
We consider the fairing design tool provided by the STR TA3 team (parameterized Myring hulls)
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 15: INNs can reliably generate diverse fairing designs for given type of shapes
Average error: 7.48%
Speed up: order of 1000X
Angle
Manta
Torpedo
Comparison of diversity between sampled and generated designs
High Diversity
T-SNE plot to compare sampled vs generated fairing shapes
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 16: INNs can reliably generate fairing designs for given drag properties
T-SNE plot to compare sampled vs generated fairing shapes
Distribution Statement A. Approved for Public Release, Distribution Unlimited
Low Drag Fairings are Faded Points

## Slide 17: Discovery of diverse shapes (UUV fairings) of comparable volume with low drag
Manta
Angle
Box fish
Tear drop
Torpedo
Whale
 | V = 1 | V = 2 | V = 5
Angle | 0.094 / 57.76 | 0.087 / 214.66 | 0.078 / 1197.91
Box | 0.048 / 58.38 | 0.044 / 217.14 | 0.039 / 1214.79
Manta | 0.062 / 56.55 | 0.058 / 210.75 | 0.052 /1182.66
Teardrop | 0.052 / 53.85 | 0.049 / 200.70 | 0.044 / 1126.55
Torpedo | 0.090 / 52.82 | 0.085 / 197.85 | 0.076/ 1106.09
Whale | 0.063 / 58.83 | 0.0.58 / 217.50 | 0.052 / 1220.82
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 18
Neural Generator
Uncertainty-quantified Variational Autoencoder
Surrogate Models
Encoder
Decoder
Design
Uncertainty
Design
Design Objectives
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 19: Hamiltonian MCMC over Design Manifold
Our approach uses exemplar designs to learn a variational encoder (VAE) where the decoder is trained with dropout. The specification network predicts the design objectives from the latent space.
The VAE and the specification network are jointly trained on the exemplar designs and their evaluation on physics models. In the design exploration stage, we condition on the new target design objectives and use temperature annealed HMC to sample the latent space, moving towards optimal designs exploiting the gradient information.
High variance/uncertainty implies off-manifold designs that may not be unrealizable.
Controlling HMC walk yields diverse designs.
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 20: OpenProp Propeller Design
Histograms of two competing design objectives. Simply sampling from the Gaussian prior in the latent space is not sufficient.
Our Approach
High efficiency at low velocity
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 21: OpenProp Propeller Design
Sample trajectories of the velocity and the propeller efficiency, as well as the corresponding variance on the objectives. Around sample ID 9000, we see high velocities with high efficiency, but the corresponding variance is high, suggesting these are unreliable designs.
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 22: Diversity in Propeller Design
Our Approach:
Creates a diverse set of propeller designs in terms number of blades, the shape of blades, pitch angles, and hub diameter.
Direct Optimization (EAs):
Creates a set of designs with a slight variation in number of blades, but the other geometric properties are similar.
Here, our design objective was to generate efficient propellers at a low velocity (efficiency higher than 75% and velocity lower than 4.5 m/s).
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 23: Diversity in Propeller Design
Here, our design objective was to generate efficient propellers at a low velocity (efficiency higher than 75% and velocity lower than 4.5 m/s).
Our Approach:
Creates a diverse set of propeller designs in terms number of blades, the shape of blades, pitch angles, and hub diameter.
Noise as a late specification: “ A 2-blade propeller produces two pressure pulses per revolution, whereas a 3-blade propeller will produce three smaller pulses per revolution for the same amount of total thrust.
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 24: Air Vehicle Design
Our approach samples designs that converge around the design objectives even though the training data and the prior distribution are far from it.
Our Approach
Our approach detects when the generates designs cannot be trusted using the specification variance.
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 25: Air Vehicle Design
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 26
Symbolic Design Synthesis
CRAIDL - a Declarative Probabilistic Programming Language
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 27: Symbolic Generator Using CRAIDL - a Declarative Probabilistic Programming Language
Kv, Kt, Km, Ir
Probability Assigned to
Each Design Rule
Leaf Nodes have Attributes that can be coupled
Diam, Pitch
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 28: Symbolic Generator Using CRAIDL - a Declarative Probabilistic Programming Language
Map leaf nodes to corpus components
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 29: Symbolic Generator Using CRAIDL - a Declarative Probabilistic Programming Language
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 30: Symbolic Generator Using CRAIDL - a Declarative Probabilistic Programming Language
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 31: Symbolic Generator Using CRAIDL - a Declarative Probabilistic Programming Language
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 32: Symbolic Generator Using CRAIDL - a Declarative Probabilistic Programming Language
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 33
Minimizing Oracle Calls Using Surrogates
Intertwined generation of data and design optimization
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 34: Iterative Feedback to Data Generator from Exploration
NS Generator: Stochastic Grammar for CRAIDL design language
Grammar Rules
Stochastic
Parameters
Example Designs
Oracles for evaluating design
Scientific models
Good Designs
Bad Designs
Need to make data generator objective-aware – Only a small percentage of designs meet the specification when the initial stochastic grammar. E.g. SwRI pipeline – out of 5000 designs, only 70 were valid. Direct tuning can lead to collapse of diversity.
Need to make evaluation faster - Scientific models can be slow to evaluate.
Need more valid designs for learning of rules and parameters – Feed valid designs back to learn the generator to improve valid generation but without losing diversity.
Design Specification
Distribution Statement A. Approved for Public Release, Distribution Unlimited
Notes: Direct tuning can lead to collapse of diversity.

## Slide 35: System-Level Surrogates
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 36: Generative Models for Design Topology
CRAIDL design language
Grammar Rules
Stochastic
Parameters
Example Designs
36
Hierarchy of Oracles
Scientific models
ML models
Symbolic rules
Good Designs
Bad Designs
Good Designs
Bad Designs
Design Specification
(Ability to hover)
100,000 ~ order of minutes
21,000
79,000
36.5 days compute
Automate retraining of Stochastic Grammar to make it more directed
Enables successful learning design patterns
The transformer model saved 137.2 days of compute time
Distribution Statement A. Approved for Public Release, Distribution Unlimited
Notes: Direct tuning can lead to collapse of diversity.

## Slide 37: Results on Program (TA3) Corpus and Hackathons
Distribution Statement A. Approved for Public Release, Distribution Unlimited
Top Down Design:
Topology design followed by tuning component params
Bottom Up Design:
Component design followed by assembly

## Slide 38: SwRI Athens Corpus: UAV/UAM
Composition to Generate Seeds
Topology Generation
Design Patterns
Propulsion
System
UAV/UAM design
FDM Input:
Abstracted topology, propulsion,
control surfaces, Mass, Inertia
Max-Distance
Hover-time
Thrust, Lift
Mission
Specifications
Abstracted
Specifications
Control: Parametric
Thrust/Lift
Position
Velocity
Final
Parameter Tuning
Geometry
Parameter Tuning
Design Flow
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 39: 5 High Performing Designs
Beetle, Score: 7962
Daisy, Score: 5218
Frog, Score: 7920
Frog, Score: 5263
Water strider, Score: 5218
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 40: 5 Top Creative Designs
Kite, Score: 4308
PrayingMantis, Score: 4944
Frog, Score: 3550
Vulture, Score: 5263
Walrus, Score: 5306
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 41: UAV Designs over the Program
Fall 2021
Spring 2022
Fall 2022
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 42: Diversity Summary Statistics
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 43: Nautilus STR Corpus: UUV
Battery
CFD and Fairing design
Pressure vessel design
Component Layout, Buoyancy, Roll/Pitch
Planning (and Control)
UUV design
Drag coefficient, force
Propeller efficiency
Power capacity
Energy profile
Path planning
Altitude planning
Energy requirement
Time requirement
Speed requirement
Mission
Specifications
Abstracted
Specifications
Propeller Opt
Manual
Component
Selection for
Mission
Design Flow
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 44: UUV Design
Total distance travelled: 4257km
Minimum distance to shore: 4810m from (80.74, -79.36)
Minimum sensing distance: 7.5km
Total distance travelled: 4827.5km
Minimum distance to shore: 1445m from (81.34, -89.94)
Robust Plan and Controller
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 45: UUV Design
Vehicle Rendering
Metric | Value
Energy Consumed | 201.2 KWh
Valid Path and Mission Complete | True
Energy Remaining | 50.3 KWh
Deployment x, y, z | (80.38, -85.11, -480)
Deployment Accuracy | 84 meters from bottom
Mission Duration | 55.9 days
Distance Travelled | 5310 km
Number Navigation Points | All navigation points met
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 46: UUV Design: Physical Design
CAD Model
Top
Key Vehicle Attributes | 
Length (m) | 4.99m
Max diameter (m) | 1.65m
Mass (kg) | 1357.1 Kg
CoB-CoG offset (m) | 0.050
Hotel power (W) | 19
Max vehicle speed (m/s) | 1.1
Side
Top
PV
Foam
OBS
Pitch shifter
DVL
CTD
Altimeter
Acoustic Comms
Names are color coded with the color of the rendering.
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 47: UUV Design: Physical Design Change from Ch0.5 to Ch1.0
Side
Ch1
Ch0.5
Major Change
PVs became larger to carry larger battery.
More floats to compensate.
Fairing was already large enough.
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 48: UUV Design: Pressure Vessel Design with Stiffners
PV1
Shape – Cylinder with spherical end caps Length – 1.0m Outside-diameter – 0.40m Stiffner_width – 0.0043m Stiffner_height – 0.0261m Stiffner_type – External e – 0.00038 Cylinder-thickness – 0.0079m Internal radius – 0.192m Sphere-thickness – 0.00452m Internal-volume – 146.3L Mass – 39.90kg Material – Al. 7075-T73 Depth-rating – 1000m with 1.3 safety factor Internal volume to mass ratio – 3.67
Depth rating: 1300m include 30% safety margin
PV use stiffeners and we used Vern’s model.
PV rendering does not show stiffeners.
PV1
Shape – Cylinder with spherical end caps Length – 1.0m Outside-diameter – 0.389391m Stiffner_width – 0.003505m Stiffner_height – 0.027245m Stiffner_type – External e – 0.00038 Cylinder-thickness – 0.007408m Internal radius – 0.187287m Sphere-thickness – 0.004394m Internal-volume – 137.714L Mass – 35.9486kg Material – Al. 7075-T73 Depth-rating – 1000m with 1.3 safety factor Internal volume to mass ratio – 3.830845
Ch0.5
Ch1
Overall, the wall thickness increases as the volume requirement also increases. Additionally, we can see that designs without stiffeners have a higher wall-thickness compared to designs with stiffeners.
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 49: UUV Design: Faring
Teardrop fairing: lower drag, better packing
Length | 4.990 m
Diameter | 1.650 m
Nose length | 1.5 m
Body length | 0.378 m
Tail length | 3.122 m
Pressure field
Velocity field
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 50
TA1 | Metric |  | NuSymCORE | Phase 1 | Phase 2 | Phase 3
TA1.1: Design Space Construction | Design space size (mined design variants) |  | Over 100,000 Topology (Air) Millions Parametric | 100’s | 1,000’s | 10,000’s
TA1.2: Design Composition | Autocomplete partial designs (completeness/ accuracy) | Connections | Topology – 100% | 50%/80% | 90%/90% | 100%/95%
 |  | Interface Components | Propulsion Chain – 100% | 40%/80% | 70%/90% | 90%/95%
 |  | Functional Components | Pressure Vessel – 100% Faring – 80% (identify parameter space manually) | 20%/80% | 50%/90% | 80%/95%
TA1.3: Design Space Exploration | Domains jointly explored |  | Multiple – Control, Energy, Structural | Multiple (2) | Multiple (3) | Multiple (4)
 | Designs explored (combinatorial + parametric) |  | Millions of Design | 1,000’s (Automated) | 100,000’s (Automated) | 1,000,000’s (Automated)
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 51: TA2 Interaction: SRI TA2 Team (Worked together on UAV and UUV)
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 52: TA2 Interaction: CRA JARVIS (UAV)
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 53: TrinityAI Designs vs DALL-E-2
TrinityAI
DALL-E-2
Distribution Statement A. Approved for Public Release, Distribution Unlimited

## Slide 54: Publications (available at https://nusci.csl.sri.com/publication/ )
Key Research Publications
Edmond Cunningham, Adam Cobb, Susmit Jha. Principal Manifold Flows. 39th International Conference on Machine Learning (ICML), 2022.
Cobb, Adam; Roy, Anirban; Elenius, Daniel; Koneripalli, Kaushik; Jha, Susmit. On Diverse System-Level Design Using Manifold Learning and Partial Simulated Annealing. 17th International Design Conference (DESIGN), 2022. Identified as Top 10% of papers at the venue.
Cobb, Adam; Roy, Anirban; Elenius, Daniel; Jha, Susmit. Trinity AI Co-Designer. Design Automation for CPS and IoT (DESTION 2022).
Chenxi Yang, Swarat Chaudhuri (2022). Safe Neurosymbolic Learning with Differentiable Symbolic Execution. International Conference on Learning Representations (ICLR), 2022
Agrawal, A., & McComb, C. Comparison of Visualization Strategies for High-Dimensional Exploration Behavior of CPS Design Agents. Design Automation for CPS and IoT (DESTION 2022).
Agrawal, A., & McComb, C (2022). Reinforcement learning for efficient design space exploration with variable fidelity analysis models. Journal of Computers and Information Science in Engineering, 2022.
Li, M., & McComb, C. Using Physics-Informed Generative Adversarial Networks to Perform Super-Resolution for Multiphase Fluid Simulations. Journal of Computers and Information Science in Engineering, 2021
Samuel Kessler, Adam Cobb, Stefan Zohren, Stephen J. Roberts. Can Sequential Bayesian Inference Solve Continual Learning? Advances in Approximate Bayesian Inference (ABI), 2021
Thank you!
Distribution Statement A. Approved for Public Release, Distribution Unlimited